## Slide 1
The CUDA ClusterFinder
Khalil Daniel Ferjaoui
Paul Scherrer Institut · aare
August 2026
Kernel design · hardware limits · seven optimization steps

## Slide 2
AARE · HYBRID PIXEL DETECTORS · CUDA CLUSTERFINDER
The kernel was never the bottleneck — feeding it was
One kernel, one thread per pixel, and seven steps to keep it fed
The stencil was fast almost immediately: at 3×3 the kernel needs 5.5 µs per frame while getting that frame across PCIe costs 16.6 — 13.2 even uncontended. The frame is gated by the wire, not the arithmetic. Six of the seven steps get data in, get results back, and measure honestly.
WHERE THIS ENDS UP — THE SHIPPED f32 BUILD AFTER ALL SEVEN STEPS · ENGINE TIMES [f32 · s4] · RECONCILED IN A1
×9.1
VS 24-THREAD CPU
61,312
FRAMES / SECOND
16.3 µs
PER FRAME, END TO END
6 / 23 M
CLUSTER MISMATCH VS CPU TWIN
RTX 4090 (Ada, sm_89) · PCIe 4.0 ×16 · Mönch 400×400 uint16 · 3×3 clusters · 100 000 frames · Cu fluorescence, MAX IV

## Slide 3
CONTEXT · WHAT THE CODE DOES
What the kernel does, and what limits it
No optimizations yet, only what the hardware has to do.
COMING UP
3–4
The algorithm
5–6
The two machines
7–8
The CUDA kernel
9–10
The hardware limit

## Slide 4
THE ALGORITHM · WHAT IT IS FOR
A photon is not a pixel — it is a cluster
3 / 34
• Charge from one absorbed photon spreads over neighbouring pixels. Summing that 3×3 patch recovers the photon energy; a single pixel does not.
• The histogram of those cluster energies is the measurement: peak position and width give the detector's gain and energy resolution.
WHY IT MATTERS
Cluster-energy spectra from an energy scan, against allpix² simulation. Each peak is one beam energy; its width is the resolution being measured.
PIXELS PER FRAME
400 × 400 = 160 000
PEAK PIXELS = PHOTONS / FRAME
~2 330 · 1.5 %
PIXELS ABOVE 5Σ (2.4 PER PHOTON)
~5 700 · 3.6 %
Real MOENCH data, Cu fluorescence, MAX IV beamtime. One cluster is emitted per local maximum, so 2 330 counts photons, not lit pixels; the recorded 3×3 windows cover 12.7 % of the frame.

## Slide 5
THE ALGORITHM · PER FRAME
Per pixel: subtract, threshold, update the pedestal
4 / 34
• Per pixel: subtract a running pedestal (mean ± rms), keep pixels above nσ · rms, cut a 3×3 cluster around each local maximum.
• 400×400 = 160 k pixels, 312.5 kB per frame; Cu data yields ~2 330 clusters per frame at 3×3.
• The pedestal is updated by every pixel that sees no photon — about 80 % of them — every frame, so the arithmetic and the data movement are coupled.
THE WHOLE ALGORITHM · THREE OUTCOMES, NOT TWO
// the whole algorithm, per pixel
v = frame[i] - pedestal_mean[i]
rms = pedestal rms at i
m = max(v) over the 3x3 window at i
if (m > nSigma * rms) // a photon is within reach
if (v == m) -> emit cluster // ... and I am its peak
else -> nothing // ... I am in its shadow
else -> update pedestal // I saw nothing
Thesis of this talk: the compute was fast almost immediately. Six of the seven steps are about feeding it.
THE SHAPE OF THE WORK
WORK ITEMS PER FRAME
160 000
OPERATIONS ON EACH
~5, identical
COMMUNICATION BETWEEN THEM
none
ORDER THEY MAY RUN IN
any
What a pixel does never depends on what its neighbours decided, only on what they measured. That one property is what the next two slides point two very different machines at.

## Slide 6
THE MACHINE WE ARE STARTING FROM
CPU: latency-oriented, built to finish one thread fast
5 / 34
Count the boxes: 6 fetch/decode, out-of-order instruction selection, two levels of private cache, all of it to keep two instruction streams fed. The ALUs are the small part.
One core, schematically. Intel Skylake is shown. The Zen 4 core in this machine differs in detail (4 FP pipes rather than 3; AVX-512 double-pumped on 256-bit datapaths) but not in kind: ~6-wide front end, 4 scalar ALUs, 2 SMT contexts, private L1 + L2. Load/store units not drawn. After Stanford CS149, Fall 2025.
PC-MOENCH-04 · AMD RYZEN 9 7950X
CORES × SMT
16 × 2
CPU, 1 THREAD
1.75 ms
CPU MT, 24 THREADS
148 µs
THAT IS THE BAR
6 762 frames / s
Thread count is swept per cluster size, not assumed: 24 at 3×3, 32 at 9×9.
Notes: The CPU slide. The point is not that CPUs are bad -- it is what the
silicon is SPENT on.
Six fetch/decode units, an out-of-order instruction selector, branch prediction
(not even drawn), L1 + L2 private cache: all of that machinery exists to find
independent work INSIDE one instruction stream, and to hide memory latency
behind a cache. It is the right design when you have a few threads that must
each finish fast.
Our problem has the opposite shape: 160 000 work items that are already
independent. We do not need a machine to FIND the parallelism -- it is handed to
us. Every transistor spent looking for it is a transistor not doing arithmetic.
On the thread sweep: 6 762 FPS is the best of a measured sweep (perf/cpu_threads.py),
not a default. 48 threads on 16 cores is 24 % SLOWER than 24 -- worth saying out
loud, because an oversubscribed baseline is the easiest way to inflate a GPU
speedup without lying about anything.

## Slide 7
THE MACHINE WE ARE MOVING TO
GPU: throughput-oriented, the whole frame at once
6 / 34
AD102 · 144 blocks, 128 enabled on this card. One SM boxed.
Same grammar, inverted proportions: 4 fetch/decode for 64 warp contexts and a wall of lanes. Nothing reorders instructions: when a warp stalls on memory, the selector just runs a different one.
One SM: a V100 is shown; this card's is the same idea (128 FP32 lanes, 48 warp slots, 100 kB shared memory). Note how few of the units are FP64, and remember it at opt7. Diagrams after Stanford CS149, Fall 2025.
NVIDIA GEFORCE RTX 4090
FP32 LANES
16 384
128 SMS × 128 LANES
vs 32 CPU streams
RESIDENT THREAD SLOTS
196 608
THE FRAME NEEDS
160 000 → all at once
Device memory runs at 1 008 GB/s (384-bit, 21 Gbps); PCIe delivers 25. Two copy engines, so H2D and D2H run at the same time.
Notes: The GPU slide, and the number to land.
128 SMs x 1 536 threads = 196 608 thread slots that can be RESIDENT at the same
time. Our frame is 160 000 pixels. The entire frame fits in the machine at once,
one thread per pixel, with room left over -- which is why slide 7's "one thread
per pixel" is not a figure of speech, and why slide 9 can talk about occupancy
as a real quantity (3x3 achieves 100 %: 1 536 threads resident per SM).
Latency hiding, in one sentence: the CPU hides memory latency with a cache and
out-of-order execution; the GPU hides it by having 48 other warps ready to run.
That is why there is no reorder buffer on this diagram and no branch predictor.
The trap to pre-empt: 16 384 lanes vs 32 streams is a factor of 512, and we
measure x9.1. Say so before someone else does. We are not lane-limited; we are
BANDWIDTH-limited -- 1 TB/s of device memory, and 25 GB/s of PCIe to reach it.
That gap between 512 and 9 IS the talk.

## Slide 8
THE CUDA KERNEL · EXECUTION MODEL
One thread per pixel
7 / 34
1 load tile + halo
›
2 __syncthreads
›
3 stencil reduction
›
4 classify
›
5 append or update pedestal
• A 16×16 block = 256 threads covers 256 pixels; the grid tiles the whole 400×400 frame. Cluster geometry is a template parameter, so the stencil is fully unrolled at compile time.
• The output is sparse: only detections touch global memory, through one atomic bump of a per-frame counter. The decision work is dense: every pixel is tested, independently and identically.
• That is exactly the shape a GPU wants: regular, independent, repeated 160 000 times per frame.
LAUNCH CONFIGURATION · ClusterFinderCUDA.hpp
block = dim3(BLOCK_X, BLOCK_Y); // 16 x 16
grid = dim3((ncols + BLOCK_X - 1)/BLOCK_X,
(nrows + BLOCK_Y - 1)/BLOCK_Y);
device::find_clusters_in_single_frame<<<grid, block, shmem, stream>>>(
d_frame, d_pd_mean, d_pd_sum, d_pd_sum2, d_pd_off, n_pd_samples,
nSigma, nrows, ncols, d_clusters, d_cluster_count, max_clusters);
400×400 pixels → a 25×25 grid of 16×16 blocks = 625 blocks per frame, handed to 128 SMs. Nothing about the launch depends on how many clusters the frame happens to contain, which is what makes the work uniform.
THREE OUTCOMES, NOT TWO
// ClusterFinder.hpp — the serial CPU
if (max > nSigma * rms) {
if (value < max)
continue; // Not max go to the
// next pixel — but
// also no pedestal
// update
} else {
pedestal.push_fast(iy, ix, ...);
}
That comment is verbatim from the CPU source. A pixel in a photon's shadow is neither recorded nor fed back — and the CUDA kernel reproduces it exactly.
~80 % of threads update the pedestal: every pixel with no photon in its window. ~1.5 % are peaks, ~18 % are shadow. The update, not the cluster write, dominates.

## Slide 9
THE CUDA KERNEL · SHARED MEMORY
Load the tile once, reuse it nine times
8 / 34
• Neighbouring threads need overlapping 3×3 windows. Without shared memory each pixel would be fetched from global memory up to nine times.
• Each block stages a tile of (16 + 2r) × (16 + 2r) pedestal-subtracted values, the halo is the price of the stencil, and it is loaded cooperatively by the threads on the block edges.
clusterfinder_kernel.cuh
extern __shared__ unsigned char smem[];
auto *sh = (COMPUTE_TYPE*)smem;
auto stride = blockDim.x + 2*col_radius;
auto tid = (threadIdx.y + row_radius)*stride
+ (threadIdx.x + col_radius);
// pedestal subtraction fused into the load
sh[tid] = d_frame[gid] - d_pd_mean[gid];
Only odd cluster sizes are supported (3×3, 5×5, 7×7, 9×9), so that the centre pixel is unique and local-maximum suppression is well defined.
The tile is stored in COMPUTE_TYPE (float), not in the pedestal type: 1.3 KB for 3×3, 2.3 KB for 9×9, against 100 KB of shared memory per SM. Even the old double-precision tile only reached 4.5 KB.
Halo cost falls with block size: 56 % of the tile at 8×8, 27 % at 16×16, 13 % at 32×32, which is the first half of the block-size argument. The second half is registers, next slide.

## Slide 10
HARDWARE · OCCUPANCY
3×3 reaches 100 % occupancy, 9×9 only 33 %
9 / 34
BLOCK SIZE
16 × 16
THREADS / BLOCK
256
MAX THREADS / SM · 48 WARPS
1 536
REGISTERS / SM
65 536
SHARED MEM / BLOCK
1.3 – 2.3 KB
16×16 is the balance point, enough threads to amortise the halo, few enough that 6 blocks still fit per SM. At 3×3 that is 48 of 48 warps resident: fully occupied. Shared memory never binds; registers do.
Shipped f32 build, measured not estimated: cuobjdump -res-usage for registers and spills, cudaOccupancyMaxActiveBlocksPerMultiprocessor for blocks/SM. RTX 4090 (sm_89). Reproduce: python/tests/perf/kernel_resources.py

## Slide 11
HARDWARE · THE REAL LIMITER
Occupancy is a means, not the goal
10 / 34
• The limiter is register pressure: every thread keeps a private clusterData[CSX × CSY] staging array, so demand grows with the square of the cluster size. 3×3 costs 38 registers, 9×9 costs 128.
• Zero spills either way. ptxas would rather give up occupancy than spill to local memory, and on this kernel that is the right trade.
• Low occupancy is not automatically a problem: at 9×9 one kernel nearly fills the machine on its own.
Occupancy is an output. At 9×9 the register file is full at two blocks, so two thirds of the thread slots are stranded: nothing else can be resident no matter how much work is queued.
HOW THESE NUMBERS WERE OBTAINED · READ FROM THE BUILT .SO, NO REBUILD
cuobjdump -res-usage build/aare/_aare_cuda*.so | c++filt
3x3: REG:38 STACK:0 LOCAL:0 # STACK/LOCAL 0 = no spills
9x9: REG:128 STACK:0 LOCAL:0
python python/tests/perf/kernel_resources.py # blocks/SM, runtime check
REGISTER BUDGET · SM_89 · F32
3×3 · OCCUPANCY
100 %
9×9 · OCCUPANCY
33 %
SPILLS, EITHER CASE
0 bytes
3×3 ON THE F64 BUILD
47 regs → 83 %
Which is why the 9×9 kernel is the one worth optimising, see opt7.
Notes: The arithmetic behind the bars, and the one caveat.
One SM holds 65 536 registers and 1 536 thread slots. A 16x16 block is 256
threads, so a block costs regs_per_thread x 256 registers. At 3x3 that is 9 728,
six blocks fit, and the THREAD SLOTS run out first at 100 %. At 9x9 it is
32 768, so two blocks exactly fill the REGISTER FILE and strand two thirds of
the slots. Same kernel, same block size, opposite binding resource.
The caveat on "low occupancy is fine": it is build-dependent. On the shipped f32
build the 9x9 kernel is long enough that four streams overlap by only 1.02x, so
the extra streams buy nothing in kernel concurrency. On the f64 build the kernel
is 3.5x longer and DOES overlap, 1.32x, and there four streams genuinely lower
the floor. Quote the overlap factor, never "occupancy is fine" on its own.
Build dependence of the register count itself: the f64 pedestal costs 3x3 nine
extra registers (47), which loses a block per SM and drops it to 83 %. 9x9 is
unmoved at 128 -- there the limiter is the clusterData[9][9] staging array, not
the pedestal, which is why opt7 helps 3x3's occupancy and not 9x9's.

## Slide 12
ROADMAP
Three acts, ordered by which bar is tallest
11 / 34
ACT I · FEED THE GPU
the host cannot submit work fast enough at 3×3 [f64]
opt1
First CUDA port
1 stream, one launch per frame
×2.34
opt2
Streams + batching
4 streams, 2 000-frame batches
×3.66
opt3
Pipeline rework
sync barriers removed
×4.32
opt4
Pinned memory
DMA-speed host transfers
×5.69
ACT II · GET THE RESULTS BACK
the host copy is now the tallest bar at 3×3 [f64]
opt5
Host↔GPU overlap
chunked submit / collect
×7.45
opt6
Zero-copy collection
read in place, never copy
×8.65
ACT III · THE KERNEL
the kernel is the tallest bar — at 9×9 at 9×9 [f32]
opt7
FP32 pedestal + variance rewrite
the only kernel change in the deck
kernel −41%
Speedups are 3×3 vs the best CPU configuration, 24 threads. Two routes were measured and rejected, two result transports inside Act II, shown next to the step they lost to, and CUDA Graphs, which is in the annex. The rule that predicts the wins predicts the failures too.

## Slide 13
ACT I OF III · FEED THE GPU
The host cannot submit work fast enough
The kernel was fast almost immediately. This act is about the host, and it is told at 3×3, where the wire is the floor.
STARTING FROM
6 762 FPS
24-thread CPU · 14.8 s for 100 000 frames
COMING UP
12
opt1 · first port
13
opt2 · streams + batching
14
opt3 · no barriers
15
opt4 · pinned memory

## Slide 14
ACT I · OPT1 · THE FIRST CUDA PORT
The first port runs at 26 % of the GPU's floor
12 / 34
• Shared-memory tiling with halo loading for any cluster size; pedestal subtraction fused into the tile load.
• Cluster geometry is a compile-time template parameter → the 3×3 stencil is fully unrolled.
• One cudaMemcpy in, one kernel, one cudaMemcpy out; the host blocks on every frame.
ClusterFinderCUDAOpt2.hpp · find_clusters()
// one frame at a time, the host waits at every step
cudaMemcpy(d_frame, h_frame, bytes, cudaMemcpyHostToDevice);
find_clusters_in_single_frame<ClusterType, FRAME_TYPE>
<<<grid, block, shmem>>>(d_frame, d_pd_mean, ...);
cudaMemcpy(h_out, d_out, out_bytes, cudaMemcpyDeviceToHost);
PCIe is full-duplex: H2D, kernel and D2H run on independent engines and overlap, so the floor is max(H2D, kernel, D2H), never the sum. Each term is that engine's busy time per frame at 4 streams, the union of its intervals, not how long one operation takes. At 3×3 [f64 · s4]: max(16.17, 15.17, 7.69) = 16.2 µs → 61 859 FPS. That max is a profiled estimate, so the deck's floor is the lower of it and the best sustained rate — the same 16.17 here; A1 shows where the two part at 9×9.
OPT1 · 3×3 · 100 K FRAMES · F64
THROUGHPUT
15 807 FPS
VS 24-THREAD CPU
×2.34
PER FRAME
63.3 µs
THE GPU FLOOR
61 859 FPS
% OF FLOOR
26 %

## Slide 15
ACT I · OPT2 · STREAMS AND BATCHING
Four streams and 2 000-frame batches: ×1.56
13 / 34
• A stream is an ordered queue of GPU work. Work in different streams may overlap, so a copy can run while another stream computes.
• Each stream gets its own StreamContext: device frame buffer, output buffer and pedestal. Frames are handed out round-robin.
• The host now submits 2 000 frames per call instead of one.
ClusterFinderCUDA.hpp · per-stream state
struct StreamContext {
cudaStream_t stream;
FRAME_TYPE *d_frame; ClusterType *d_clusters;
PEDESTAL_TYPE *d_pd_mean, *d_pd_sum, *d_pd_sum2;
};
auto &sc = v_sc[frame_idx % n_streams]; // round-robin
Scaffolding, not yet the payoff. The streams exist, but the host still synchronises after every round: see opt3.
OPT2 · 3×3 · 4 STREAMS · BATCH 2 000
THROUGHPUT
24 726 FPS
VS 24-THREAD CPU
×3.66
PER FRAME
40.4 µs
STEP GAIN OVER OPT1
×1.56
% OF FLOOR · 61 859 FPS
40 % (was 26)

## Slide 16
ACT I · OPT3 · REMOVE THE SYNC BARRIERS
One sync per batch, not one per round: ×1.18
14 / 34
• opt2 synchronised all streams after every round of n_streams frames. The GPU drained to empty each time.
• opt3 submits every frame's H2D → kernel → D2H asynchronously, then synchronises once at the end of the batch.
THE ONE-LINE IDEA
// opt2: barrier after every round
for (round) {
submit(n_streams frames);
cudaDeviceSynchronize();
}
// opt3: submit everything, sync once
for (frame : batch) {
cudaMemcpyAsync(..., sc.stream);
kernel<<<..., sc.stream>>>(...);
cudaMemcpyAsync(..., sc.stream);
}
for (sc : streams)
cudaStreamSynchronize(sc.stream);
29 188 FPS · ×4.32 34.3 µs/frame · 47 % of floor (was 40)
Each lane is one stream. Removing the barrier lets a stream start its next frame while its neighbours are still copying. The three panels are scheduled, not sketched: H2D and D2H are one FIFO engine each, so a stream waits for the copy engine, never for another stream's copy to finish overlapping it.

## Slide 17
ACT I · OPT4 · PINNED (PAGE-LOCKED) MEMORY
Pinning the input buys DMA-speed H2D: ×1.32
15 / 34
• Normal host memory is pageable: the OS may move or swap it. A DMA engine cannot safely read that, so the driver first copies your data into a hidden pinned staging buffer. Every transfer is copied twice.
• Pinning locks the pages in physical RAM. The GPU's DMA engine then reads host memory directly, no staging copy, and the transfer can be truly asynchronous.
ClusterFinderCUDA.hpp
// pin the whole dataset once
cudaHostRegister(ptr, bytes,
cudaHostRegisterDefault);
// ... run the whole campaign ...
cudaHostUnregister(ptr);
38 486 FPS · ×5.69 26.0 µs/frame · 62 % of floor, the largest step in Act I
Measured H2D [s1, uncontended]: one 400×400 uint16 frame (312.5 KiB = 320 000 B) in 13.2 µs = 24.2 GB/s, 77 % of PCIe 4.0 ×16 theoretical, i.e. true DMA speed. In the shipped pipeline it reads 16.6 [s4], +26 % of H2D↔D2H contention (A1). Pageable staging runs ~15 GB/s.
The rule, first sighting: ×1.32 at 3×3 but only ×1.02 at 9×9. Pinning attacks H2D, the tallest bar at 3×3, the shortest at 9×9.

## Slide 18
ACT II OF III · GET THE RESULTS BACK
The host copy is now the tallest bar
Frames go in at DMA speed. The results still come back slowly. Still 3×3 — but 9×9 is where this act pays most.
ARRIVING AT
38 486 FPS
opt4 · 26.0 µs per frame · 62 % of the GPU floor
COMING UP
16
opt5 · host↔GPU overlap
17
opt6 · zero-copy
18
two rejected routes

## Slide 19
ACT II · OPT5 · HOST↔GPU OVERLAP
Overlapping host and GPU hides min(host, GPU): ×1.31
16 / 34
• opt3 overlapped H2D ∥ kernel ∥ D2H across streams, inside one batch, but never the host with the GPU: find_clusters_batched synchronised, then built thousands of ClusterVectors with the GPU idle.
• opt5 keeps one batch in flight while materialising the previous one: chunk i+1 is submitted before chunk i is collected.
The time hidden is min(GPU, host), so this pays most when the two are comparable, and cannot rescue a host term that is simply larger.
OPT5 · 3×3 AND 9×9 · NO CUDA WORK AT ALL
3×3 THROUGHPUT
50 410 FPS
PER FRAME · STEP · OF FLOOR
19.8 µs · ×1.31 · 81 %
9×9 THROUGHPUT
15 063 FPS
PER FRAME · STEP · OF FLOOR
66.4 µs · ×1.20 · 45 %
For clusters that must outlive the finder, this is the endpoint at 3×3: opt6 lends, it does not give.
Notes: opt5 — host<->GPU overlap. Code and chunk sizing are on annex A3.
tok = cf.submit_batch(data[a0:b0], first_frame=a0)
for a, b in bounds[1:]:
nxt = cf.submit_batch(data[a:b], first_frame=a) # GPU starts N+1 ...
results.extend(cf.collect(tok)) # ... host unpacks N
tok = nxt
results.extend(cf.collect(tok)) # drain
1. This is now INTERNAL to find_clusters_batched(), so every caller gets it for
free. submit_batch/collect stay public for anyone who wants the token by hand.
2. The chunk size is rounded to a multiple of n_streams, because the device
pedestal is per-stream: an uneven chunk would advance the four stream
pedestals by different amounts and the finders would stop being comparable.
Why the gain differs by cluster size: the saving is min(GPU, host) per chunk, so
it is largest when the two terms are comparable. At 3x3 they nearly are (GPU
16.2 us, host ~9.8) and opt5 is worth x1.31. At 9x9 the host term is roughly
twice the GPU term, so overlap hides only the smaller one and opt5 is worth
x1.20 - which is exactly the diagnosis that motivates opt6: you cannot overlap
your way out of a host term that is simply larger. Report SS8.2.

## Slide 20
ACT II · OPT6 · ZERO-COPY COLLECTION
Read the results in place: ×2.21 at 9×9
17 / 34
• The D2H lands in a pinned host buffer. collect() then allocates one ClusterVector per frame and memcpys into it; at 9×9 that is 467 kB per frame, ~9.3 GB per run, single-threaded.
• collect_view() returns a BatchView: strided numpy views straight onto the pinned buffer. It withholds ownership past the chunk, not access, every cluster's payload and coordinates are readable.
The win is max(0, host copy − GPU floor): at 3×3 the 8 µs copy hides under a 16.2 µs floor and opt5 had already absorbed most of it; at 9×9 the 40 µs copy is larger than the floor and cannot hide at any overlap.
The two bars are the competing costs, not the two steps; the step times are on the right.
OPT6 · 3×3 AND 9×9 · COLLECT_VIEW()
3×3 THROUGHPUT
58 495 FPS
PER FRAME · STEP · OF FLOOR
17.1 µs · ×1.16 · 95 %
9×9 THROUGHPUT
33 323 FPS
PER FRAME · STEP · OF FLOOR
30.0 µs · ×2.21 · 100 %
opt5 → opt6: 19.8 → 17.1 and 66.4 → 30.0 µs, bit-identical, 0.2 % spread, zero warm faults. FLOOR = lower of the s4 engine max and the best sustained rate: at 3×3 the 16.17 µs max sets it; at 9×9 f64 the run BEATS the 32.66 µs max, so the 30.0 sustained sets it [A1].

## Slide 21
ACT II · TWO REJECTED ROUTES
The copy is allocation-bound, not bandwidth-bound
18 / 34
B′
One allocation per chunk
collect_packed()
Removes the per-frame malloc but keeps the copy, and the copy is ~80% of the cost. Worse, the replacement allocation is 1.17 GB, far above glibc's mmap threshold, so it is mmap'd and munmap'd every chunk: 606 566 faults, ~21 µs/frame.
69.3 µs · deleted from the API
B″
Parallel materialisation
8-thread copy pool
Each worker gets its own glibc arena, which destroys the cross-run heap reuse that makes the single-threaded path cheap. Faults went 9 700 → 2 270 000; MALLOC_ARENA_MAX=1 collapsed them back to 138 k, which is the proof.
+6% at best, −33% when results are freed promptly
Copying faster does not help when the cost is the OS populating pages. The only winning move is not to allocate — which is exactly what opt6 does. materialize_slot() is deliberately single-threaded and carries a comment saying so, to stop the experiment being repeated.

## Slide 22
ACT III OF III · THE KERNEL
Only now is the kernel the tallest bar
The story moves to 9×9. At 3×3 the wire was always the floor and the kernel never mattered; at 9×9 it is the tallest bar, which is why this act exists.
ARRIVING AT
58 495 FPS
opt6 · 3×3, and 33 323 FPS at 9×9, where this act pays
COMING UP
19
opt7 · FP32 pedestal
20
the correctness trap
21
the variance rewrite
22
why it comes last

## Slide 23
ACT III · OPT7 · FP32 DEVICE PEDESTAL
FP32 halves pedestal traffic: −41 % kernel time
19 / 34
• ~80 % of pixels take the pedestal-update branch: it reads off, sum, sum² and writes back sum, sum², mean. All four pedestal arrays are DEVICE_PED_TYPE, so one typedef halves every one of those six accesses — 48 bytes per updating pixel in FP64, 24 bytes in FP32.
• The kernel is bandwidth-bound, so halving that traffic nearly halves the time.
• Second effect: on a GeForce part, FP64 arithmetic runs at 1/64 of FP32. The pedestal update was paying that tax on every pixel.
• Third, quietly: the narrower accumulators free 9 registers at 3×3, 47 → 38, which buys back a block per SM and takes occupancy 83 % → 100 %.
ONE TYPEDEF
// clusterfinder_kernel.cuh
using COMPUTE_TYPE = float;
using DEVICE_PED_TYPE = float;
// was: double
Kernel, 9×9 [s1 · cap 1700 · exclusive] 39.86 µs → 23.70 µs (−40.5%) Shipped [s4]: 30.0 → 25.1 µs end to end.
Both panels, both builds, same git rev, 20 000 frames. The deck's rule, and the reason there are two: quote s1 for how long an engine takes, s4 for which one sets the floor. A1 has the full grid.
Naive FP32 is wrong (next two slides), and even when correct it only pays because Act II came first.
At 3×3 the same typedef is worth −70.6 % (14.72 → 4.32 µs [s1]) yet buys only 4.6 % end to end: there the kernel was never the tallest bar.

## Slide 24
ACT III · OPT7 · THE CORRECTNESS TRAP
The naive FP32 pedestal loses the variance to cancellation
20 / 34
• The running variance was computed as var = E[X²] − mean². With a pedestal mean of ~4 655 ADU, both operands are ≈ 2.17 × 10⁷ while the answer is ≈ 2 000.
• In FP32 each operand sits on a grid of 2 ADU², so the answer inherits ±3 — an absolute error that does not shrink. For a pixel whose true variance is 9 that is a third of it; below rms ≈ 2 it goes negative and the rms clamps to 0.
WHAT IT LOOKED LIKE
EXTRA CLUSTERS
+28.06%
Quiet pixels got rms → 0, so their threshold became 0 and they fired on every single frame, producing a large unphysical high-energy tail in the spectrum.
AFFECTED PIXELS
~1–2% of the sensor
WRITTEN UP IN
docs/pedestal_precision_…

## Slide 25
ACT III · OPT7 · THE VARIANCE REWRITE
Accumulate what is small, not what is large
21 / 34
• Freeze a per-pixel baseline X₀ = round(mean) once, at the end of pedestal training, and never move it again.
• Accumulate the centred value Y = X − X₀ instead of X, and report the mean as X₀ + sum/n — so nothing downstream changes.
clusterfinder_kernel.cuh
// before: both terms ~2.17e7, answer ~2000
var = sum2/n - mean*mean;
// after: centred on a frozen per-pixel offset X0
DEVICE_PED_TYPE resid = mean - d_pd_off[i]; // ~O(1)
DEVICE_PED_TYPE var_px = sum2[i]/n - resid*resid; // no cancellation
Result: the 100% FP32 build now matches the FP64 build to 3 × 10⁻⁷, 70 clusters out of 233 million.
WHY IT WORKS
Precision is relative. Floats resolve small numbers finely and large numbers coarsely, so never let a small answer be the difference of two large numbers.
F32 VS F64 COUNTS
3 × 10⁻⁷
VS CPU
0.0039%
X₀ must never be updated: the accumulators are defined relative to it.

## Slide 26
ACT III · WHY THIS ACT COMES LAST
The saving never grew — the frame around it shrank
22 / 34
The same typedef saves −4.63 µs at opt4 and −4.87 µs at opt6 — the two readings whose fault counts match. What changes is the denominator: the frame falls 79.8 → 30.0 µs, so an identical saving reads −5.8 %, then −16.2 %. Act II did not make the kernel win bigger; it made it separable.
And the act ends by handing the floor away. At s4, the config that ships, the f64 arm is kernel-bound: 32.66 against a 25.25 µs D2H. The typedef puts the kernel at 23.94 — below a D2H that never moved. The constraint is now the result path, not the arithmetic. [engines: 19/34]
9×9 · 20 000 frames · 4 streams · cap 1 700 · warm · both arms at the same git rev. opt3 is excluded: its two arms sat in different allocator states, so that comparison does not report the typedef at all. † opt5's arms differ the same way; its reading agrees with the other two but is not independently attributable. Both are worked through in annex A4. The f32 bar at opt6 is opt7, the shipped build; the f32 bars at opt4 and opt5 are the same typedef applied at earlier steps — configurations that exist only to make this comparison controlled.

## Slide 27
RESULTS · WHAT CAME OUT OF IT
The whole ladder, and how to use it
Both cluster sizes end to end, and the audit behind the numbers.
ARRIVING AT
58 495 FPS
opt6 · everything after this is the ladder seen whole
COMING UP
23–24
Results, both cluster sizes
25
Where the time went
26–27
What the numbers survived

## Slide 28
RESULTS · 3×3
×9.1 at 3×3, sitting on the H2D floor
23 / 34
×9.1 over 24 CPU threads, 14.8 s → 1.63 s for 100 000 frames, and at the H2D floor.
Every step is monotonic, and correctness is held constant throughout, 0.004 % against the CPU baseline, and exact against the CPU twin that isolates the port (slides 28–31).
3×3 clusters · nσ = 5 · 100 000 frames · batch 2 000 · 4 streams · 5 reps · warm = best of reps 1–4 (collect() does not converge, it oscillates between allocator states) · each step in its own process · CPU baseline = ClusterFinderMT at its best thread count, 24 here, first pass only.

## Slide 29
RESULTS · 9×9
×26.5 at 9×9, and opt7 hands the floor to D2H
24 / 34
×26.5 over 32 CPU threads; the kernel is the tallest bar for the whole f64 arm, and opt7's −40 % drops it below D2H.
opt4 buys ×1.03 here and ×1.32 at 3×3. Same code, opposite regimes, the rule, twice.
9×9 · cap 1 700 (lossless; 1 500 truncated 0.0095 % of clusters) · 20 000 frames · opt1/opt2 are 3×3-only · CPU baseline ClusterFinderMT at 32 threads. The floor is the lower of the nsys estimate and the best sustained rate; both arms are sustained-bound, corroborated to 8.8 % (f64) and 0.4 % (f32). Why the arms differ: 544.5 kB of D2H costs 25.2 µs on both [s4], hidden under the 32.7 µs f64 kernel, not under the 23.9 µs f32 one.

## Slide 30
WHERE THE TIME ACTUALLY WENT
The host bar dies first, then the floor itself drops
25 / 34
Acts I and II never touch the arithmetic. The GPU floor is a flat 16.2 µs at 3×3 / 30.0 µs at 9×9; what collapses is everything stacked on it.
Act III is the only step that lowers the floor itself, and it could not have been seen until the stack above it was gone.
Blue/white/amber = the GPU floor for that act's build — the LOWER of the s4 engine max (max of H2D, kernel, D2H; PCIe is full duplex, so never the sum) and the best sustained rate. At 3×3 the engine max sets it, 16.17 µs; at 9×9 f64 the sustained rate does, 30.01 against a 32.66 µs max. Grey = everything the host adds on top. At 9×9 the host contributes +50 µs at opt3 and nothing at opt6.

## Slide 31
BEHIND THE NUMBERS · WHAT THEY HAD TO SURVIVE
Three ways a GPU benchmark lies
26 / 34
First-touch page faults
Each run materialises ~10 GB of clusters. The first pass faults in ~2.6 M pages at 0.7 µs each, up to 4 s of pure OS work inside the timer.
Fix: re-run until getrusage() minor faults plateau (< 200 k).
CUDA-event kernel timing
avg_kernel_time_ms() measures elapsed time on a stream, including waiting for other streams. Under 8-stream load it over-reads by up to 3.5×.
Fix: Nsight Systems per-instance times; 1 stream for exclusive numbers.
The profiler itself
Under nsys, wall time per frame inflates ~4× from API tracing.
Fix: GPU op times from nsys, wall times from unprofiled runs.
THE FAULT PROTOCOL · python/tests/ClusterFinderCUDA_perf.ipynb
# every timed cell in the benchmark notebook is bracketed with:
mf0 = resource.getrusage(resource.RUSAGE_SELF).ru_minflt
... t = time.perf_counter() - t0 ...
print(f'minor faults: {mf1-mf0:,}') # quote the run where this plateaus
Validated: wall = steady-state + faults × 0.68 µs reproduced a 6.110 s run to within 1 ms. Kernel time stayed constant throughout; the GPU was never the variable.

## Slide 32
BEHIND THE NUMBERS · WHAT A USER ACTUALLY GETS
A first run loses a third of its throughput to page faults
27 / 34
Everything that materialises clusters loses a third of its throughput on the first run, +7 to +20 µs per frame, depending on how much of it the GPU can hide behind its own work.
Only the two ends escape, for opposite reasons. opt1 never grows the heap: it discards each frame. opt6 never needs one, and reaches 98 % of its peak on a cold process.
Single pass, one process, every ClusterVector retained, python/tests/ClusterFinderCUDA_perf.ipynb, f32, the same 100 000 frames. Not the campaign's "cold" rep, which discards results and so never grows the heap. Repeat the run and the amber bars climb onto the blue ones; opt1 and opt6 never move, because neither ever paid.

## Slide 33
VALIDATION · DOES IT FIND THE SAME PHOTONS
Every number so far assumed the answers are identical
Whether the CUDA finder returns the same clusters as the CPU.
ESTABLISHED
×9.1 and ×26.5
on the hardware floor at both cluster sizes, if the physics holds
COMING UP
28–29
The fair comparison
30–31
The residual, dissected
32–33
For users
34
What is next

## Slide 34
VALIDATION · WHY A CPU TWIN WAS NEEDED
CPU and CUDA update the pedestal at different moments
28 / 34
The serial CPU finder updates the pedestal as the raster scan reaches each pixel. A CUDA thread cannot: 160 000 of them read the pedestal at once, so the update is applied at the frame boundary.
So a straight CPU↔CUDA comparison moves two things at once. ClusterFinderFrozen is the serial finder with only the update moved to the frame end: same arithmetic, same gates, same scan.
Frozen is a diagnostic twin, not a product: it exists so the next two slides can attribute each disagreement to exactly one cause. cpu vs frozen = update timing; frozen vs cuda = the port. Every finder on these slides is trained on the same 1 000 pedestal frames and run over the same 10 000 data frames.
Notes: Why this slide is here.
The obvious experiment - run the CPU finder and the CUDA finder over the same
frames and count the differences - cannot answer the question anyone actually
asks, which is "is the port correct?" It moves two variables at once:
1. WHEN the pedestal is updated. The serial CPU finder updates per pixel,
during the raster scan, so a pixel late in the frame is judged against a
pedestal that already contains this frame's earlier pixels. That is
scan-order dependent by construction.
2. WHAT arithmetic runs. float vs double, a different local-max expression,
a different rounding point.
ClusterFinderFrozen holds (2) fixed and changes only (1): it is the serial
finder, same decision logic line for line, with the update deferred to the frame
boundary. That is the CUDA update model, on the CPU.
So the three-way comparison factorises:
cpu vs frozen -> update timing alone (19 of 23.2 M)
frozen vs cuda -> the port alone (6 of 23.2 M)
and the second is the number that answers the question. It is also why the
headline mismatch figure in this deck is 6 / 23 M and not 25 / 23 M: the larger
number is dominated by an effect that has nothing to do with CUDA.
Frozen ships in the library as a diagnostic, not as the recommended finder.

## Slide 35
VALIDATION · ISOLATING ONE VARIABLE AT A TIME
CUDA and its CPU twin agree exactly: 0 in 23 million
29 / 34
• ClusterFinderFrozen makes byte-for-byte the same decisions as ClusterFinder and differs in exactly one thing: when the pedestal is updated. Frozen per frame, pushed at frame end. That is the CUDA model, so comparing against it isolates everything else the port changes.
COMPARISON
THE ONE THING THAT DIFFERS
A-ONLY / B-ONLY
% OF CLUSTERS
serial CPU vs frozen CPU
update timing alone: a CPU-only effect
8 / 11
0.000082 %
serial CPU vs CUDA [f64 ped]
the same thing, and nothing else
8 / 11
0.000082 %
frozen CPU vs CUDA [f64 ped]
nothing
0 / 0
0 %
frozen CPU vs CUDA [f32 ped]
the float32 pedestal EMA drifting: see next slide
0 / 6
0.000026 %
Identical, frame by frame. 23 244 605 clusters, not one disagreement, and cpu vs cuda equals cpu vs frozen exactly, so the port adds nothing of its own. Payloads: 99.9941 % bit-identical, worst case 1 ADU on one pixel.
The 0.004 % headline is the baseline disagreeing with itself. ClusterFinderMT builds 48 ClusterFinders, each with its own Pedestal, after 100 k frames each has ~2 083 updates, not 100 000. It measures the baseline, not the port.
3×3 · 10 000 frames · 23.2 M clusters · same pedestal, same frames · exact centre-set difference at tol = 0 · python/tests/validation_tiers.py. [f64 ped] and [f32 ped] are the same source built with DEVICE_PED_TYPE double / float; COMPUTE_TYPE is float in both, so the stencil arithmetic is identical across the two rows.

## Slide 36
VALIDATION · THE DISAGREEMENT, SEEN
The whole disagreement is one duplicate centre
30 / 34
Only the 3×3 footprints of each finder's own centres are drawn, everything else is blank, so the panels differ exactly where the finders do. Values are pedestal-subtracted ADU.
cuda's patch is one row taller: a second centre directly below the one both found, so the two 3×3 windows overlap. The charge is already counted: a duplicate, not a new photon.
Frame 147, the strongest of the six residuals · shipping f32 build · every other centre in the patch agrees, including the ordinary photon at bottom right.
Notes: The masked view, and how to read it.
Each panel masks every pixel that is not inside the 3x3 footprint of one of THAT
finder's own cluster centres. So a pixel is visible on the left only if frozen
claimed it, and visible on the right only if cuda did. Where the panels look
identical, the finders agreed pixel for pixel.
The red dots are cluster centres. The amber ring is the one centre cuda keeps
that frozen does not: (202, 8), directly below (202, 7) which both finders keep.
Because the two 3x3 windows overlap, cuda's patch is four rows tall where
frozen's is three - that visible extra row IS the disagreement.
Note what is NOT happening: there is no cluster in one panel that is absent from
the other's neighbourhood entirely. Nothing was missed, and nothing was invented
out of noise. The two finders are arguing about which of two adjacent pixels owns
a photon they both found.
Same construction as helper.plot_masked_mismatch() in the notebook, so this is
reproducible from ClusterFinderFrozen_vs_CUDA.ipynb directly.

## Slide 37
VALIDATION · THE SIX RESIDUALS, DISSECTED
float32 cannot tell these two pixels apart
31 / 34
THE ONLY TEST THAT FLIPS, AND WHY
frame 147 centre (x=202, y=8) 3×3 window
raw window (ADU) pedestal-subtracted, 1 decimal
[[4646 5282 4703] [[ 45.3 638.4 -12.1] frozen and cuda
[4857 5318 4950] [ 43.7 638.4 -7.5] print the SAME
[4763 4640 4858]] [ 1.1 70.7 136.4]] window
the two contenders, at full precision:
rival (dy=-1) centre
frozen [f64 ped] 638.383019956 638.382773664
cuda [f32 ped] 638.382812500 638.382812500
gate: accept if centre >= max(window)
frozen 638.382773664 >= 638.383019956 -> reject
cuda 638.382812500 >= 638.382812500 -> ACCEPT
Separation under the f64 pedestal: 0.000246 ADU. One float32 ULP at 4 679.6 ADU is 0.000488. The two pixels are half a ULP apart; in float32 they are *the same number*, and the gate accepts on a tie.
With the f64 pedestal there are none at all. In the shipping f32 build each of the six sits one pixel from a cluster both finders found, a duplicate neighbour, never a spurious photon and never a missed one.
The same frame 147 as the previous slide, recomputed under each finder's decision-time pedestal. Both finders run the same gate (CPU value == max, CUDA !(val < max)), so the tie separates them, not the expression.
Notes: Frame 147, centre (x=202, y=8). The full numbers.
centre rival centre - rival
frozen (f64 host ped) 638.382773664 638.383019956 -0.000246291
cuda (f32 dev ped) 638.382812500 638.382812500 0.000000000
pedestal mean, centre: f64 4679.617226336 f32 4679.617187500
pedestal mean, rival : f64 4643.616980044 f32 4643.617187500
1 float32 ULP at 4679.6 ADU = 0.000488 ADU
the f64 separation between the two pixels = 0.50 ULP
Read that last line slowly: the two pixels differ by HALF a float32 ULP. There is
no float32 number between them, so once the pedestal is stored as float32 they
round to the identical bit pattern. The local-max gate is `value >= max`, which
accepts on equality - so CUDA keeps the centre and frozen, which can still see
the rival is 2.5e-4 ADU higher, rejects it.
This is not drift in the usual sense. It is not that the f32 EMA wandered away
from the f64 one over thousands of updates - look at the pedestal columns, they
agree to 4e-5 and 2e-4 ADU. It is that the QUESTION being asked ("which of these
two pixels is larger?") has an answer that float32 cannot represent.
Consequences worth stating out loud if asked:
- It is one-directional. cuda-only 6, frozen-only 0. A tie can only ever ADD a
centre, never remove one, because >= accepts.
- All six are at Chebyshev distance 1 from a cluster both finders found: a
duplicate neighbour, never a spurious photon.
- With DEVICE_PED_TYPE = double the residual is 0 / 0 at both 3x3 and 9x9.
- Fixing it in f32 would mean a strict > in the gate, which changes the CPU's
documented behaviour on genuine ties. Not worth 6 clusters in 23 million.

## Slide 38
FOR USERS · PYTHON API
The fast path in eight lines
32 / 34
THE RECOMMENDED PATTERN
from aare import File, ClusterFinderCUDA
cf = ClusterFinderCUDA(image_size=(400, 400), cluster_size=(3, 3),
n_sigma=5, n_streams=4,
max_clusters_per_frame=3000)
for _ in range(1000): # 1. train the pedestal
cf.push_pedestal_frame(pd.read_frame())
data = f.read_n(100_000) # 2. one contiguous array
cf.register_input_buffer(data) # 3. pin it once
for s in range(0, N, 2000): # 4. batch through it
clusters = cf.find_clusters_batched(data[s:s+2000], first_frame=s)
cf.unregister_input_buffer() # 5. release the pages
• find_clusters_batched returns one ClusterVector per frame, in order, and does opt5's chunked overlap internally, so you get it for free.
• register_input_buffer is what turns opt3 into opt4: one call.
IF YOU REDUCE AS YOU GO
# opt6: never copy
for v in cf.find_cluster_views_
batched_iter(data, 2000):
hist.fill(v.sums())
# views die with the chunk
×1.16 at 3×3, ×2.21 at 9×9. The views expose every cluster; they only withhold ownership past the chunk.
Pin once, outside the loop. Slices of a registered array inherit the pinning.

## Slide 39
FOR USERS · CHOOSING THE KNOBS
Four knobs, and the one that silently truncates
33 / 34
PARAMETER
WHAT IT DOES
GUIDANCE
n_streams
How many frames may be in flight at once — an upper bound, not a count: the copy engines cap the real number below it.
4 at both sizes. 8 buys no kernel concurrency at 9×9 (+1% instance time) and inflates the CUDA-event timer 3.5×.
max_clusters_per_frame
Fixed size of the per-frame D2H transfer.
Must exceed the real maximum or clusters are silently dropped, and it sets the D2H bar directly. Measured at 9×9: the maximum is 1 633, and the lossless cap of 1 700 already makes D2H the bottleneck on the f32 build.
batch size
Frames per find_clusters_batched call.
2 000 amortises launch overhead without a large pinned footprint.
cluster_size
Compile-time stencil geometry.
3×3 and 9×9 are registered; 9×9 moves the bottleneck off H2D and onto the kernel on f64, and onto D2H once opt7 shortens it.
register_input_buffer
Page-locks the host array for DMA.
Always, if the data is already in RAM. Check the pinning budget first.
The single most common mistake: leaving max_clusters_per_frame too low. It does not error; it truncates, and every frame quietly returns the same count.

## Slide 40
WHERE THIS LEAVES US
The bottleneck has walked from the host, to the GPU, to the wire
34 / 34
DONE
×9.1 at 3×3, ×26.5 at 9×9
16.3 and 25.1 µs/frame end to end, both on their hardware floor. Against the CPU twin that isolates the port the decisions are identical; the shipping f32 pedestal adds 6 duplicates in 23 million.
DONE
FP32 pedestal, safely
−40.5% kernel, and correct, because the variance is now accumulated on a frozen per-pixel offset instead of a raw second moment.
NEXT
3×3: transfer granularity
The 16.31 µs sustained sits 3.16 µs above the uncontended 13.15 µs H2D rate [f32: s4 vs s1]: 2 000 separate 320 kB descriptors, plus 26% of H2D↔D2H contention.
NEXT
9×9: the result path, not the kernel
At a lossless cap D2H already binds [f32 · s4]: 25.24 µs against a 23.94 µs kernel. More kernel work buys nothing until the D2H slot stops being cap-sized.
Full numbers, methodology and reproduction steps: docs/ClusterFinderCUDA_benchmark_results.md · notebook python/tests/ClusterFinderCUDA_perf.ipynb · measurement campaign python/tests/perf/

## Slide 41
ANNEX · THE EVIDENCE BEHIND THE CLAIMS
Kept back so the arc stays readable
The measurement artefacts, the rejected route, and the opt5 code.
EVERYTHING SO FAR
34 slides
the arc is finished; what follows answers questions
COMING UP
A1
Every engine number, reconciled
A2
CUDA Graphs, and why they lost
A3
opt5 · the overlap code
A4
The fault model, tested
A5
The three benchmark artefacts

## Slide 42
A1
ANNEX · MEASUREMENT CONVENTION · EXPANDS SLIDE 12
Uncontended, or as the pipeline runs it
A1
• Every engine time in this deck is tagged [build · s1|s4]. s1 is one stream with nothing else running: what an engine does on its own, which is the right number for a capability claim and for the headroom that remains. s4 is the shipped four-stream pipeline: each engine's busy time per frame, the union of its intervals — the only number that can set a floor.
3×3 · µS/FRAME
S1 F64
S1 F32
S4 F64
S4 F32
H2D
13.14
13.15
16.17
16.63
kernel
14.72
4.32
15.17
5.53
D2H
5.31
5.27
7.69
7.57
engine max [s4]
—
—
16.17
16.63
FLOOR = lower of max, sustained
—
—
16.17
16.31
9×9 · CAP 1700
S1 F64
S1 F32
S4 F64
S4 F32
H2D
13.20
13.22
20.77
20.54
kernel
39.86
23.70
32.66
23.94
D2H
21.97
21.95
25.25
25.24
engine max [s4]
—
—
32.66
25.24
FLOOR = lower of max, sustained
—
—
30.01
25.14
Two traps this table closes. (1) s4 is engine *occupancy*, not duration — the 9×9 kernel row falls 39.86 → 32.66 while every transfer rises, and nothing that measures a duration falls under load. (2) the FLOOR is not the engine max: the max is profiled and runs 2–8 % high, so the floor is whichever is lower, it or the best unprofiled sustained rate — which is why opt6 reports 30.01 µs against a 32.66 max.
THE D2H SHIFT IS AN s4 PHENOMENON: at s1 the kernel binds in BOTH arms (39.86 and 23.70 against a 21.97 / 21.95 D2H); only under four-stream contention does D2H climb to 25.24 and overtake the 23.94 f32 kernel. Any claim about which engine binds must be read from the s4 columns. NEITHER DIRECTION IS FASTER THAN THE OTHER. At s1, H2D moves 320 000 B in 13.15 µs = 24.3 GB/s; D2H moves 120 004 B in 5.27 µs = 22.8 GB/s; at 9×9 D2H moves 557 604 B in 21.95 µs = 25.4 GB/s. All sit at 72–81 % of PCIe 4.0 ×16's 31.5 GB/s, the smallest transfer paying the most fixed cost per byte — so a taller bar always means MORE BYTES, never a slower wire. That is why cap 1 700 hands the 9×9 floor to D2H. Source: probes.csv in perf/results/2026-08-18_{f64,f32}/ (3×3) and 2026-08-20_{f64,f32}_capAB/ (9×9). The floor is the LOWER of the s4 estimate and the best unprofiled sustained rate — 16.31 vs 16.63 at 3×3 f32, 25.14 vs 25.24 at 9×9 f32 — so a probe roofline is never a hard denominator.

## Slide 43
A2
ANNEX · REJECTED ROUTE · CUDA GRAPHS · EXPANDS SLIDE 11 · 1 OF 2
CUDA Graphs, a sound idea that the next act overtook
A2 · 1/2
• Every cudaMemcpyAsync / kernel launch costs the CPU a few microseconds of driver work, per frame and per operation. After opt4 that looked like the budget.
• A CUDA Graph captures the whole dependency DAG once. Replaying it is a single cudaGraphLaunch: the driver already knows every node and edge.
ClusterFinderCUDA_graph.hpp
// record once, at setup
cudaStreamBeginCapture(sc.stream, ...);
submit_h2d_kernel_d2h(sc);
cudaStreamEndCapture(sc.stream, &sc.graph);
cudaGraphInstantiate(&sc.graphExec, ...);
// per batch: one call
cudaGraphLaunch(sc.graphExec, sc.stream);
REJECTED 3×3: 39 752 FPS, inside noise of opt4. 9×9: 11 072 FPS, 12 % slower.
Its 3×3 edge was never established: the graph finder recorded no CUDA events while the stream finder did, and that instrumentation tax (2.8 µs) is larger than the gap (0.8 µs). More decisively, it never received the chunked pipeline of opt5, so it is competing on ~2 µs of launch cost against a 24 µs floor. Launch overhead stops binding one step later; the technique aimed at it can no longer pay.

## Slide 44
A2
ANNEX · REJECTED ROUTE · CUDA GRAPHS · 2 OF 2
What a CUDA Graph actually saves, in microseconds
A2 · 2/2
• The stream path issues four runtime calls per frame, a memset to clear the cluster counter, H2D, the launch, D2H. A graph replaces all four with one cudaGraphLaunch, so the ceiling on what it can save is ¾ of the submission cost.
CALL
PER FRAME
HOST COST
µS/FRAME
cudaMemcpyAsync
2
1.98 µs
3.97
cudaLaunchKernel
1
2.13 µs
2.13
cudaMemsetAsync
1
1.57 µs
1.57
submission total
4
7.67
THE ARITHMETIC
7.67 us/frame x 3/4 = 5.75 us/frame eliminated, AS MEASURED (under nsys)
5.75 / 4 (see A5) ~ 1.4 us/frame eliminated, unprofiled estimate
~1.4 µs against a 16.17 µs floor = 8.7 %, real while the host is the critical path, and worth nothing after opt5, which hides host work under the GPU entirely.
ROUTE A · MEASURED VERDICT
3×3 VS OPT4
×1.03
9×9 VS OPT4
×0.88
VS OPT5 AT 9×9
36 % behind
Read from CUPTI_..._RUNTIME, the host table, so this is the one order-of-magnitude number in the deck, ±50 %. It is enough to show graphs cannot pay against a 16 µs floor, and not enough to quote to two figures.

## Slide 45
A3
ANNEX · OPT5 · THE OVERLAP CODE · EXPANDS SLIDE 16
The overlap, in six lines, and why you never write them
A3
THE WHOLE OF OPT5
tok = cf.submit_batch(data[a0:b0], first_frame=a0)
for a, b in bounds[1:]:
nxt = cf.submit_batch(data[a:b], first_frame=a) # GPU starts N+1 …
results.extend(cf.collect(tok)) # … host unpacks N
tok = nxt
results.extend(cf.collect(tok)) # drain the last one
• You do not write this. It is inside find_clusters_batched(), which chunks the batch and runs the loop for you, opt5 arrived as a speedup, not an API change, and every existing caller got it without editing a line.
• submit_batch() and collect() stay public for anyone who wants the token by hand, streaming from a detector, interleaving other work between chunks.
CHUNK SIZING · THE TWO CONSTRAINTS
MULTIPLE OF
n_streams
CAPPED AT
MAX_SLOT_BYTES
The chunk MUST be a multiple of n_streams. The device pedestal is per-stream and advances once per frame the stream sees, so an uneven chunk leaves the four pedestals at different ages, the finder would stop being reproducible, and two runs of the same data would not agree.
It is also capped so the two pinned output slots stay bounded: the slot is chunk × (4 + cap × sizeof(Cluster)), which at 9×9 and cap 1 700 is 544.5 kB per frame. chunk_size_for(n) applies both rules; pass the result to reserve_output_slots() to pre-pay the page-locking outside any timed region.
Two chunks in flight is enough. A third adds pinned memory and no overlap: the host is already busy for the whole time the GPU is.
The saving is min(GPU, host) per chunk, so opt5 pays most when the two terms are comparable, ×1.31 at 3×3, and least when one dominates, ×1.20 at 9×9, where the host term is roughly twice the GPU term. That gap is the diagnosis that motivates opt6 (report §8.2).

## Slide 46
A4
ANNEX · THE FAULT MODEL · EXPANDS SLIDE 22
The fault model, tested against every step
A4
• Slide 26 fits 0.68 µs per first-touch fault. If that rate is right it should predict the f64→f32 gap at every step from the fault counts alone — and where it does, the comparison is measuring the allocator, not the typedef.
STEP
F64 WARM (FAULTS)
F32 WARM (FAULTS)
Δ WALL
Δ FAULTS
PREDICTED
VERDICT
opt3
82.44 µs (128 k)
95.66 µs (521 k)
+13.22
+393 k
+13.37
the allocator
opt4
79.83 µs (128 k)
75.20 µs (127 k)
−4.63
−0.5 k
−0.02
clean
opt5
66.39 µs (152 k)
61.85 µs (10 k)
−4.54
−141 k
−4.81
not separable
opt6
30.01 µs (0)
25.14 µs (0)
−4.87
0
0.00
clean
opt3 is the whole argument in one row. A 393 k fault gap predicts +13.37 µs; +13.22 was observed — agreement to 1 %. The −40 % kernel is in there somewhere, invisible under 13 µs of the OS zeroing pages. Only opt4 and opt6, where the fault term is ~0, report the typedef at all.
ladder_9x9.csv in results/2026-08-20_{f64,f32}_cap1700/, warm = best of reps 1–4, faults are that rep's own getrusage minor-fault count. Predicted = Δfaults × 0.68 µs ÷ 20 000 frames. This table replaces an earlier figure that quoted opt3's +16 % as a measurement of the result path; it is a measurement of two allocator states, and the model above is how that was established.

## Slide 47
A5
ANNEX · BENCHMARK ARTEFACTS · EXPANDS SLIDE 26 · 1 OF 3
First-touch page faults: two sources, one counter
A5 · 1/3
• A page exists in the process's address space but has no physical frame yet. On first touch the kernel finds one, zeroes it (mandatory), and maps it. No disk I/O: ru_majflt stays 0 all campaign. At 4 kB/page, 1 GB = 262 144 faults.
(A) RESULT HEAP
(B) PINNED D2H SLOTS
allocator
malloc → mmap, one ClusterVector per frame
cudaMallocHost, in submit_batch
cost / page
0.7 µs
1.0 µs: same fault + pin + DMA map
recurs?
yes, every alloc/free cycle above the mmap threshold
no: once per buffer, for its lifetime
removed by
collect_view(): it allocates nothing
nothing; reserve_output_slots() only moves it out of the timer
The two are exactly additive. Reserving subtracts precisely the pre-pin count from run 0 and changes nothing else.
NOT A CORRELATION, AN IDENTITY
3x3: 572 292 - 455 129 = 117 163 vs 117 192 pre-pin
9x9: 2 759 037 - 2 278 567 = 480 470 vs 480 474
closed form: 2 slots x 2000 x 120 004 B / 4 kB = 117 191
At 9×9 the heap never plateaus. ~9.3 GB per pass is above glibc's mmap threshold, so it is munmap'd and re-faulted every pass: ~292 k faults ≈ 10 µs/frame, permanently. No number of re-runs removes it, which is an independent argument for opt6.

## Slide 48
A5
ANNEX · BENCHMARK ARTEFACTS · 2 OF 3
CUDA events measure the stream, not the kernel
A5 · 2/3
• avg_kernel_time_ms() brackets the launch with cudaEventRecord on the kernel's own stream. What it returns is elapsed time on that stream's timeline, which includes time spent queued behind other streams.
• So it is honest at 1 stream and inflates under saturation: up to 3.5× at 8 streams. The tell is that the derived *PCIe + overhead* = wall/N − kernel_ms goes negative: kernels overlap, so wall/frame < kernel/frame.
• It is also not free: ~3.6 µs/frame, i.e. 10–15 % of end-to-end throughput at 3×3, to produce a number that is unusable exactly when it matters.
ClusterFinderCUDA.hpp
if (m_time_kernels) // OFF by default, all 3 finders
cudaEventRecord(start[slot][i], sc.stream);
find_clusters_in_single_frame<<<grid, block, shmem, sc.stream>>>(...);
if (m_time_kernels)
cudaEventRecord(stop[slot][i], sc.stream); // <- queue-wait lands here
The flag exists for comparability, not preference: with events on for one finder and off for another, the step between them absorbs the tax.
9×9 KERNEL · F64 · NSYS
S1 · DURATION
39.86 µs
S4 · OCCUPANCY
32.66 µs
OVERLAP FACTOR
1.32×
Same kernel. The s4 column is the union of kernel intervals per frame, not how long one kernel takes. Quote s1 for duration; s4 feeds the floor, subject to the sustained-rate rule on slide 12. Full grid: A1.

## Slide 49
A5
ANNEX · BENCHMARK ARTEFACTS · 3 OF 3
Where nsys is sound, and where it is not
A5 · 3/3
• Tracing a host call means running a callback on entry and on exit, inside the interval being measured. GPU work is different: the hardware stamps its own start/end and the host reads those records afterwards, so nothing is injected into the execution path.
MEASUREMENT
SQLITE TABLE
9×9 [F64 · S1 · CAP 1500]
VERDICT
cudaLaunchKernel: the host call
CUPTI_..._RUNTIME
1.85 µs
inflated ~4×
the kernel executing
CUPTI_..._KERNEL
39.93 µs
sound to ~2 %
cudaMemcpyAsync: the host call
CUPTI_..._RUNTIME
1.65 µs
inflated ~4×
the H2D / D2H transfer
CUPTI_..._MEMCPY
13.25 / 19.44 µs
sound to ~2 %
Same cudaMemcpyAsync, two numbers: 1.65 µs to ask for the copy, 13.25 µs for the copy to happen. If the profiler must be present at the moment to measure it, it distorts it; if the hardware records it anyway and the profiler reads it later, it does not.
Every headline number in this deck (kernel times, transfer times, duty cycles, overlap and every engine floor) comes from the _KERNEL and _MEMCPY tables (see gpu_span.py). ⚠ CAP 1500 — the ONLY cap-1500 numbers left in the deck, kept because the RUNTIME column exists only in the trace and the host call cost does not depend on the cap. So the 19.44 µs D2H here is NOT the shipped 9×9 bar — at cap 1700 that engine reads 21.95 [s1] and 25.24 [s4], which is what binds the f32 build. The one figure read from _RUNTIME is the graph launch budget in A2, and it is quoted to one significant figure for exactly this reason. Proof the GPU side is sound: opt7 sustains 25.14 µs unprofiled against a 25.24 µs estimate measured under the profiler, 0.4 % apart, which a 4× distortion could not survive.